McGill University	DIGITAL SYSTEM DESIGN

Faculty of Engineering	ECSE-323

FINAL EXAMINATION

FALL  2004 (DECEMBER 2004)

ANSWER  KEY

STUDENT NAME                            McGILL I.D. NUMBER

Examiner: Prof. J. Clark 				Associate Examiner:  Prof. Frank Ferrie

Signature:						Signature:

Co-Examiner: Prof. M. Marin

Signature:

Date: December 20 , 2004                                         	  	              Time: 2:00 pm

INSTRUCTIONS:     SEE NEXT PAGE.

McGILL UNIVERSITY

Department of Electrical and Computer Engineering

ECSE-323									Fall 2004

FINAL EXAM

Question		Maximum Points	     Points Attained

1			 10

2			 15

3			 20

4			 15

5			 15

6			 15

- 15

- 15

- 15

- 20

- 15

- 10

Total		         180 points

Please write down your name:  ANSWER KEY

Please write your student ID: ______________________________________

Instructions/Please read carefully!

This is a close book exam. No books or notes are allowed. You may use a standard calculator.

All work is to be done on the attached sheets and under no circumstance are booklets or loose sheets to be used. Write your name at the top of every sheet.

Read the question carefully. If something appears ambiguous, write down your assumption. The points have been assigned according to the formula that 1 point = 1 exam minute, so please pace yourself accordingly.

Your Name_______________________________________________________

Question 1 :  CMOS Circuit Technology (10 points)

(5 points)	a)	Write the logic function produced by the following transmission gate circuit.

(5 points)	b)	Draw the equivalent CMOS circuit showing clearly the PULL-UP-NETWORK and the

PULL-DOWN-NETWORK.

_________________________________________________________________________________________

- Z = (A [(B C + B(C ] + A [(B(C + B C ] = A ( B ( C.

Your Name__________________________________________________________________________________

Question 2 :Boolean Logic Theory (15 points)

Find  h = h(x1,x2)  such that the following network structure can produce the function

f (x1,x2,x3,x4) = (m (1,2,5,6, 9,10,12,15)

(5 points) 	a)   Give the algebraic expression of   f.

(5 points) 	b)   Give the algebraic expression of  h.

(5 points)	c)   Give the minimal sum-of-products logic circuits corresponding to H and  G.

_________________________________________________________________

Your Name______________________________________________________________________________

Question 3 : VHDL (20 points)

- (10 points) Using a single selected signal assignment statement, write a complete VHDL description of a circuit that implements the Boolean function  f (x,A,B)= [x(0)x(1) + x(0)A +x(1)B]. Use x(0) and x(1) as the select inputs. Draw the equivalent multiplexer circuit.

- (10 points) Using a process block, write a complete VHDL description of an 8-bit synchronous barrel shifter circuit (a barrel shifter shifts left or right by N bits at a time, where N is an input number.  In addition to a 3-bit N input, the barrel shifter should have 8 bit parallel data input and outputs, synchronous  SHIFT_ENABLE and LOAD_ENABLE inputs, an asynchronous CLEAR, and a mode input which is 1 for left shift and 0 for right shift. LOAD operations should have precedence over SHIFT operations.

_________________________________________________________________________________________

Continue Question 3 on next page….

Your Name______________________________________________________________________________

Question 3:VHDL (20 points)

Your Name__________________________________________________________________________________

Question 4 : Combinational Circuit Synthesis (15 points)

Design a 4-bit combinational shifter circuit. This circuit has no memory elements and is purely combinational. It has 4 inputs I = (I1,I2,I3,I4) and 4 outputs  P = (P1,P2,P3,P4) and 2 control lines  S1 and S2. Each one of the four modes of operation of the shifter is selected by the corresponding values of  the control lines as described in the following table

| Mode selection | Shifter function |
| --- | --- |
| S1 S2 |  |
| 0 0 | Ii = Pi for all i (i = 1,2,3,4) |
| 0 1 | Shift right, (P1,P2,P3,P4) = (0,I1,I2,I3) |
| 1 0 | Shift left, (P1,P2,P3,P4) = (I2,I3,I4,0) |
| 1 1 | Rotate (P1,P2,P3,P4) = (,I4, I1, I2,I3) |

(5 points) a)  Give the algebraic expression of  P as a function of  I and S1,S2.

(5 points) b) Draw the minimal combinational circuit using only NAND gates

(5 points) c)  Draw the circuit of the outputs using  only  4 x 1  multiplexers and the fewest number of gates.

_________________________________________________________________________________________

Your Name______________________________________________________________________________

Question 4 : Combinational Circuit Synthesis(Continued)

Your Name_______________________________________________________

Question 5 : Testing of Combinational Circuits (15 points)

For the following circuit

(5 point)		a)	Give the check points.

(5 points)	b)	Give the test(s) for fault 4/1 using the path-sensitizing method.

(5 points) 	c)	Give the minimal test sets using the covering table and the Petrick function.

________________________________________________________

You Name_____________________________________________________________________________

Question 6: Sequential circuits (15 points)

Analyze the following circuit

(5 points)	a) 	Prove with a state-transition-diagram (4 states) that this circuit is a latch. Give the 				characteristic and excitation equations (or tables) of this latch.

(5 points)	b) 	Using the given latch circuit, draw the circuit of a J-K type latch.

(5 points)	c) 	Using the given latch circuit, draw the circuit of a T-type latch.

____________________________________________________________________________________

Your Name___________________________________________________________________________________

Question 7: Counter Design (15 points)

Design a 3-bit self-starting synchronous binary counter. This counter operates as shown in the following table:

| Clear (Cl) Load (Ld) Count (Ct) | A+ B+ C+ |
| --- | --- |
| 0 X X | 0 0 0 |
| 1 1 X | IA IB IC (load) |
| 1 0 0 | A B C (no change) |
| 1 0 1 | Present state + 1 |

where  IA  ,IB  ,IC  are the input lines and  A, B, C the outputs of the counter.

(5 points)	a)	Give the next-state equations of the counter.

(5 points)	b)	Give the excitation equations of the D-type flip-flops.

(5 points)	c)	Draw clearly the complete circuit.

Hint: Use a MUX to implement the LOAD function. Assume edge-trigger D-type flip-flops with asynchronous clear

_________________________________________________________________________________________

Your name ________________________________________________________________________________

Question 8: Circuit Implementation Strategies/Logic arrays (15 points)

Using the PAL schematic shown on the  next page, which has 4 inputs and 5 outputs, two of which may be folded,

produce the following functions:

f1 =  A D  + (A  B C

f2 =  A D  + A B C  + B C(D

f3 =   B C  + B D.

(7 points)	a)	Decompose the functions so that they can be produced with the given PAL.

(8 points) 	b)	Complete the PAL program by marking clearly the required connections.

Not all connections are needed.

____________________________________________________________________________

Continue Question 8 on next page -------------(

Your name ______________________________________________

Question 8: Circuit Implementation Strategies/Logic arrays(15 points)  (Continues)

Your Name_______________________________________________________________________________

Question 9: Finite State Machine Design(15 points)

Design a Mealey type Finite State Machine that will convert  SERIALLY a 3-bit binary input message into a 3-bit Gray code output message. Assume that the most-significant-bit of the message enters the unit first and that, after the third cycle, the machines returns to the initial state and becomes ready to accept serially the next 3 binary bits.

The code conversion table is shown below:

| Binary Code | Gray Code |
| --- | --- |
| 0 0 0 | 0 0 0 |
| 0 0 1 | 0 0 1 |
| 0 1 0 | 0 1 1 |
| 0 1 1 | 0 1 0 |
| 1 0 0 | 1 1 0 |
| 1 0 1 | 1 1 1 |
| 1 1 0 | 1 0 1 |
| 1 1 1 | 1 0 0 |

(5 points)	a)  Give the minimal state-transition-diagram of this FSM. (5 States are needed)

(3 points)	b)  Give the ONE-HOT ASSIGNMENT state-transition-table.

(4 points)	c)  Give the complete circuit  using D-type flip-flops and AND, OR, NOT gates.

(3 points)	d)  Give the formula to compute the maximum clock rate of this  FSM.

____________________________________________________________________________

Continue Question 9 on next page  -------------(

Your Name_______________________________________________________________________________

Question 9: Finite State Machine Design(15 points) (Continues)

Your Name_______________________________________________________

Question 10 : Design of Sequential Systems (20 points)

Using a synchronous Datapath/Controller approach, design a system that can factor (find all prime divisors of) a user-supplied 8-bit unsigned number using a serial algorithm. Assume that you have available to you an 8-bit divider module (with quotient and remainder outputs) as well as any other datapath elements that you might need.

- (5 points) Draw the block diagram for the system, showing all of the datapath elements and all control signals.

- (5 points) Draw the state-transition diagram for the controller.

- (10 points) Write a complete VHDL description of the system.

____________________________________________________________________________

Continue Question 10 on next page….

Your Name_________________________________________________________________________________

Question 10 (continued)

Your Name_________________________________________________________________________________

Question 10 (continued)

Your Name__________________________________________________________________________________

Question 11 :Optimization of Finite State Machines (15 points)

Consider the two following FSM’s, M and  N, whose state transition tables are shown below

M State Transition Table                                                         N State Transition Table

| Present State | Next State X = 0 X =1 | Outputs Z |
| --- | --- | --- |
| S0 | S3 | S1 | 0 |
| S1 | S0 | S1 | 0 |
| S2 | S0 | S2 | 1 |
| S3 | S0 | S3 | 1 |
| Present State | Next State X = 0 X =1 | Outputs Z |
| A | E | A | 1 |
| B | F | B | 1 |
| C | E | D | 0 |
| D | E | C | 0 |
| E | B | D | 0 |
| F | B | C | 0 |

(5 points)	a)	Reduce  M  to a minimum number of states

(5 points)	b)	Reduce  N  to a minum number of states

(5 points)	c)	Show by inspecting the reduced tables, that  N is equivalent to M.

____________________________________________________________________________

Your Name_______________________________________________________

Question 12 : Testing of Sequential Circuits (10 points)

- (5 points) Explain how LFSR circuits can be used to i) generate test vectors, ii) compute signatures of circuit responses to the test vectors.

- (5 points) Give 3 applications of the JTAG interface.